## Slide 1: 6.033 Lecture 11 Congestion Control
March 10, 2010
Key Ideas:
Sliding window protocol
Congestion control
slides: http://mit.edu/6.033/www/assignments/lec11.pdf
http://mit.edu/6.033/www/assignments/lec11.pptx

## Slide 2: Recap: At Least Once Delivery
Timeout Interval
Sender
Receiver
pkt(seqno, …)
ack(seqno, …)
pkt(seqno+1, …)
pkt(seqno+1, …)
How long to set timeout?
Too long: net underutilized
Too short: rexmit all the time
Proper setting depends on packet round trip time (RTT)
Can measure
RTT

## Slide 3: Exponentially Weighted Moving Average (EWMA)
measure = new RTT measurement
rtt = α(measure) + (1-α)(rtt) ; α = 1/8
timeout = β * rtt ; β = 2
Chart: Estimating RTT with EWMA
Raw Samples | 12 | 17 | 25 | 16 | 22 | 12 | 24 | 33 | 9 | 11 | 18 | 4 | 5 | 9 | 15
a = 1/8 | 12 | 12.625 | 14.1719 | 14.4004 | 15.3503 | 14.9315 | 16.0651 | 18.182 | 17.0342 | 16.2799 | 16.495 | 14.9331 | 13.6914 | 13.105 | 13.3419
a = 1/2 | 12 | 14.5 | 19.75 | 17.875 | 19.9375 | 15.9688 | 19.9844 | 26.4922 | 17.7461 | 14.373 | 16.1865 | 10.0933 | 7.5466 | 8.2733 | 11.6367

## Slide 4: Sliding Window in Action
Sndr
Rcvr
window = 1-5
1
2
3
4
5
p1
a1
6
window = 2-6
a2
p2

## Slide 5: Sliding Window in Action
Sndr
Rcvr
1
2
3
4
5
p1
a1
6
a3
p3
window = 3-7
a2
p2
7
window = 2-6
Send next packet as acks arrive, rather than waiting for all acks in window

## Slide 6: Still may wait
Sndr
Rcvr
1
2
3
4
5
p1
a1
6
a3
p3
a2
p2
7
window = 1-2
window = 2-3
window = 3-4
a4
p4
a5
p5
idle
idle
idle

## Slide 7: Reordering
recv(p):
slot = p.sno – head
if (slot > head + size):
drop
else:
new = isempty(slot)
if (new) add p to slot
ack p
if (slot == head and new)
deliver prefix to app
head = head+ len(prefix)
P2
P4
P5
size = 5
head= 1
head+ size
head : sno of last delivered packet
size: length of reordering queue
slot: position to insert new packet
P1
PREFIX
head= 3
P6?
Application
Reordering
Buffer

## Slide 8: Reordering
recv(p):
slot = p.sno – head
if (slot > head + size):
drop
else:
new = isempty(slot)
if (new) add p to slot
ack p
if (slot == head and new)
deliver prefix to app
head = head+ len(prefix)
P4
P5
size = 5
head= 3
head+ size
head : sno of last delivered packet
size: length of reordering queue
slot: position to insert new packet
Reordering
Buffer

## Slide 9: T=0-1
Pkt
1
2
3
Pkt | Ack’d | Timeout
1 |  | 2
2 |  | 2.33
3 |  | 2.66
4 |  | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 10: T=1-2
Pkt
1
2
3
Pkt | Ack’d | Timeout
1 |  | 2
2 |  | 2.33
3 |  | 2.66
4 |  | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 11: T=1-2
Pkt
1
2
3
Pkt | Ack’d | Timeout
1 | 1 | 2
2 |  | 2.33
3 |  | 2.66
4 |  | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 12: T=1-2
Pkt
1
2
3
Pkt | Ack’d | Timeout
1 | 1 | 2
2 |  | 2.33
3 |  | 2.66
4 |  | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 13: T=1-2
Pkt
1
2
3
4
5
6
Pkt | Ack’d | Timeout
1 | 1 | 2
2 |  | 2.33
3 |  | 2.66
4 |  | 3
5 |  | 3.33
6 |  | 3.66
7 |  | 
8 |  | 
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 14: T=2-3
Pkt
1
2
3
4
5
6
Pkt | Ack’d | Timeout
1 | 1 | 2
2 | 2 | 2.33
3 |  | 2.66
4 |  | 3
5 |  | 3.33
6 |  | 3.66
7 |  | 
8 |  | 
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 15: T=2-3
Pkt
1
2
3
4
5
6
3
7
8
Pkt | Ack’d | Timeout
1 | 1 | 2
2 | 2 | 2.33
3 |  | 4.66
4 |  | 3
5 |  | 3.33
6 |  | 3.66
7 |  | 4
8 |  | 4.33
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 16: T=3-4
Pkt
1
2
3
4
5
6
3
7
8
Pkt | Ack’d | Timeout
1 | 1 | 2
2 | 2 | 2.33
3 | 3 | 4.66
4 |  | 3
5 |  | 3.33
6 |  | 3.66
7 |  | 4
8 |  | 4.33
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 17: T=3-4
Pkt
1
2
3
4
5
6
3
7
8
4
5
6
Pkt | Ack’d | Timeout
1 | 1 | 2
2 | 2 | 2.33
3 | 3 | 4.66
4 |  | 5
5 |  | 5.33
6 |  | 5.66
7 |  | 4
8 |  | 4.33
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 18: T=3-4
Pkt
1
2
3
4
5
6
3
7
8
4
5
6
Pkt | Ack’d | Timeout
1 | 1 | 2
2 | 2 | 2.33
3 | 3 | 4.66
4 |  | 5
5 |  | 5.33
6 |  | 5.66
7 |  | 4
8 |  | 4.33
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head
Sender is spending all of its time retransmitting
Queue is filling with duplicate packets
No new transmissions are getting through!
Congestion collapse

## Slide 19: T=4-5
Pkt
1
2
3
4
5
6
3
7
8
4
5
6
7
8, 9
Pkt | Ack’d | Timeout
1 | 1 | 2
2 | 2 | 2.33
3 | 3 | 4.66
4 | 4 | 5
5 |  | 5.33
6 |  | 5.66
7 |  | 6
8 |  | 6.33
9 |  | 6.66
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 20: T=5-6
Pkt
1
2
3
4
5
6
3
7
8
4
5
6
7
8, 9, 10,11,6
Pkt | Ack’d | Timeout
1 | 1 | 2
2 | 2 | 2.33
3 | 3 | 4.66
4 | 4 | 5
5 | 5 | 5.33
6 |  | 7.66
7 |  | 6
8 |  | 6.33
9 |  | 6.66
10 |  | 7
11 |  | 7.33
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head

## Slide 21: T=6-7
Pkt
1
2
3
4
5
6
3
7
8
4
5
6
7
8, 9, 10,11,6, 7, 8,9
Pkt | Ack’d | Timeout
1 | 1 | 2
2 | 2 | 2.33
3 | 3 | 4.66
4 | 4 | 5
5 | 5 | 5.33
6 | 6 | 7.66
7 |  | 8
8 |  | 8.33
9 |  | 8.66
10 |  | 7
11 |  | 7.33
12 |  | 
13 |  | 
14 |  | 
Router Queue
Sender
Window
Head